## Slide 1
Noiseless Channels
A channel in which there are at least as many output symbols as input symbols, but in which each of the output symbols can be produced by the occurrence only of a particular one of the input symbols is called a noiseless channel. The channel matrix of a noiseless channel has the property that there is one, and only one, non-zero element in each column.:
we know, with certainty 1, which input symbol, was transmitted given knowledge of the received output symbol.
there is only one non-zero element in each column.

## Slide 2
Noiseless Channels
Mutual Information through a noiseless channel:
The mutual information for noiseless channels is given by
I(A;B) = H(A)
That is, the amount of information provided by the channel is the same as the information sent through the channel.

## Slide 3
Deterministic Channels
A channel in which there are at least as many input symbols as output symbols, but in which each of the input symbols is capable of producing only one of the output symbols is called a deterministic channel.
The channel matrix of a deterministic channel has the property that there is one, and only one, non-zero element in each row, and since the entries along each row must sum to 1, that non-zero element is equal to 1.
There is only one nonzero element in each row and that the element is 1.

## Slide 4
Deterministic Channels
Mutual Information through a deterministic channel
The mutual information for noiseless channels is given by
I(A;B) = H(B)
That is, the amount of information provided by the channel is the same as theinformation produced by the channel output

## Slide 5
Cascaded Channels
Output of channel AB is connected to the input of channel BC.
Say the input symbol ai is transmitted through channel AB,
and this produces bj as the output from channel AB.
Then bj forms the input to channel BC which,
in turn, produces ck as the output from channel BC.
The output ck depends solely on bj not on ai .
The mutual information for noiseless channels is given by
I(A;B) ≥ I(A;C) wih equality iff P(a|c) =P(a|b), when P(b,c)≠ 0
That is, channels tend to leak information and the amount of information out of a
cascade can be no greater (and is usually less) than the information from the first
channel.
If channel BC is noiseless.
I(A;B) = I(A;C)

## Slide 6
Channel Capacity: Maximum Mutual Information
Consider an information channel with input alphabet A output alphabet B and channel matrix PAB with conditional channel probabilities P(bj | ai). The mutual information:
The maximum amount of information carrying capacity for the channel is H(A), the amount of information that is being transmitted through the channel. But this is reduced by H(A | B), which is an indication of the amount of “noise” present in the channel.
The expression for mutual information depends not only on the channel probabilities, P(bj | ai). which uniquely identify a channel, but also on how the channel is used, the input or source probability assignment P(ai).
As such I(A;B), cannot be used to provide a unique and comparative measure of the information carrying capacity of a channel since it depends on how the channel is used.
One solution is to ensure that the same probability assignment (or input distribution) is used in calculating the mutual information for different channels.

## Slide 7
Channel Capacity: Maximum Mutual Information
The maximum average mutual information, I(A;B) in any single use of a channel defines the channel capacity. Mathematically,
the channel capacity, , is defined as:
that is, the maximum mutual information over all possible input probability assignments.

## Slide 8
Shannon–Hartley theorem
In information theory, the Shannon–Hartley theorem tells the maximum rate at which information can be transmitted over a communications channel of a specified bandwidth in the presence of noise.
The theorem establishes Shannon's channel capacity for such a communication link, a bound on the maximum amount of error-free information per time unit that can be transmitted with a specified bandwidth in the presence of the noise interference, assuming that the signal power is bounded, and that the Gaussian noise process is characterized by a known power or power spectral density.
The Shannon–Hartley theorem states: “the channel capacity C, meaning the theoretical tightest upper bound on the information rate of data that can be communicated at an arbitrarily low error rate using an average received signal power S through an analog communication channel subject to additive white Gaussian noise (AWGN) of power N”:

## Slide 9
Shannon–Hartley theorem
C: is the channel capacity in bits per second, a theoretical upper bound on the net bit rate (information rate, sometimes denoted I);
B: is the bandwidth of the channel in hertz (passband bandwidth in case of a bandpass signal);
S: is the average received signal power over the bandwidth (in case of a carrier-modulated passband transmission, often denoted C), measured in watts (or volts squared);
N: is the average power of the noise and interference over the bandwidth measured in watts (or volts squared);
S/N: is the signal-to-noise ratio (SNR) or the carrier-to-noise ratio (CNR) of the communication signal to the noise and interference at the receiver (expressed as a linear power ratio, not as logarithmic decibels).

## Slide 10
Examples:
Q1: At a SNR of 0 dB (Signal power = Noise power) the Capacity in bits/s is equal to the ……………………………in hertz.
Q2: If the SNR is 20 dB, and the bandwidth available is 4 kHz, which is appropriate for telephone communications, then C = ?
Q3: If the requirement is to transmit at 50 kbit/s, and a bandwidth of 10 kHz is used, then the minimum S/N required is ?